## Slide 1: Orinoquia River basin vulnerability assessment
Preliminary results
Hydrosystem Research Group, UMass
02-24-2025

## Slide 2: Objectives
Assess the vulnerability of the Orinoquia River basin to climate and demand change
Provide insights of potential adaptation or policies to reduce vulnerability and risk
Methods Resilience by Design (Brown et al. 2020)

## Slide 3: Schematic of the model chain used for the vulnerability assessment
Climate generator
Hydrology
Cultivated land projections
Rice
Oil palm trees
Freshwater rural demand
Population growth projections
Rural
Urban
Livestock population growth projections
Irrigation demand
Livestock demand
Chicken
Pigs
Cattle
Rainfall
Temperature
PET
Orinoquia Water Future (OWF) model
Simulated water deliveries to each users across all 27 sub-basins
River flow downstream each of the considered sub-basins
Policies
Freshwater urban demand

## Slide 4: Orinoquia Water Futures’ model
Inputs:
  Streamflow time series for each of the 27 sub-basins
  Demand (freshwater, irrigation, livestock) time series
Outputs:
  Deliveries to each customer types across all 27 sub-basins
  Streamflow downstream each sub-basin

## Slide 5: Climate Stress Test - Scenarios
A comprehensive sensitivity analysis to change in climate and demand to reveal thresholds or tipping points from which the system is no longer able to reach its objectives
Future climate scenarios (Temp., Rainfall) are obtained by perturbing current climate realizations obtained from the climate generator. Additive factors are used for temperature and multipliers are used for rainfall
Future demand scenarios (freshwater, irrigation and livestock) demand are obtained by linearly extrapolating historical trends. The ‘baseline’ value is the one obtained for the year 2022.
Policy scenarios are used to represent different distribution “strategies” among users.

## Slide 6: Policies
First Come First Served (FCFS) This dispatch order is meant to represent the way water is currently allocated to the different users across the basin. This is not the allocation intended by the state government.
  Urban customers
  Agricultural customers
  Livestock customers
  Rural customers
  Minimum flow requirements not enforced
Policy enforced (PE) This dispatch order is meant to represent the allocation the wants to be respected across the basin:
  Minimum flow requirements enforced
  Urban customers
  Rural customers
  Agricultural customers
  Livestock customers

## Slide 7: Climate Stress Test - Range
 | Climate Scenarios |  |  | Water demand scenarios |  |  | Policies
Drivers of change | Climate variability | Temperature | Rainfall | Population growth (urban and rural) (Including CI) | Cultivated land (rice and oil palm tree) | Livestock population growth (chickens, pigs, cattle). | Dispatch order (i.e., setting a preference to users to define which gets water first)
Range or scenarios | 5 stochastic realizations of 50 yrs | From 0oC to +5oC with an increment of +1oC | From 30% reduction to an increase by 30% with an increment of 10% | In addition to baseline (2022), projected values for the year 2030, 2040 and 2050 | In addition to baseline (2022), projected values for the year 2030, 2040 and 2050 | In addition to baseline (2022), projected values for the year 2030, 2040 and 2050 | First Come First Served (FCFS) Policy Enforced (PE)
Number of scenarios | 5 | 6 | 7 | 4 | 4 | 4 | 2
Total number of simulations = 5 x 6 x 7 x 4 x 4 x 4 x 2 = 26,880

## Slide 8: Climate projections CMIP6
SSP5 8.5
Historical period: 1985-2014 (30 years)
Two future periods
  Near future: 2026-2055 (30 years)
  Far future: 2056-2085 (30 years)

## Slide 9
Random sampling from joint distributions Gaussian copula (marginals: Beta distributions for T, and Gamma distribution for P)
Random samples (x1000) will be used for establishing the distributions of the performance metrics merging the stress test and the information from CMIP6

## Slide 10: Water demand scenarios and assumptions

## Slide 11: Urban Demand Scenarios and assumptions
Population thresholds | System complexity | Demand per day and capita (Liter/day/cap)
 | Low | 100
 | Medium | 125
 | Medium-high | 135
 | High | 150
Population thresholds | System complexity | Demand per day and capita (Liter/day/cap)
 | Low | 100
 | Medium | 125
 | Medium-high | 135
 | High | 150
Source to support the assumption in Table 1:
https://www.minvivienda.gov.co/sites/default/files/documentos/titulo_d.pdf
https://comunidad.udistrital.edu.co/javalerof/files/2015/09/titulo_d_version_prueba.pdf
Table 1: Water demand per day and habitant in urban areas
Urban freshwater demand calculated by multiplying population and per day and capita consumption is increased by 50% (i.e., multiplied by 1.5) to account for demand from commercial and industrial sectors
A 25% loss term is accounted for (i.e., calculated demand is multiplied by

## Slide 12: Rural Demand Scenarios and assumptions
Population thresholds | System complexity | Demand per day and capita (Liter/day/cap)
 | Low | 100
Population thresholds | System complexity | Demand per day and capita (Liter/day/cap)
 | Low | 100
Source to support the assumption in Table 1:
https://www.minvivienda.gov.co/sites/default/files/documentos/titulo_d.pdf
https://comunidad.udistrital.edu.co/javalerof/files/2015/09/titulo_d_version_prueba.pdf
Table 1: Water demand per day and habitant in rural areas
Rural areas are always assumed as ‘low’ complexity (i.e., per capita and per day demand equals 100).
No multiplier applied for commercial and industrial
A 25% loss term is accounted for (i.e., calculated demand is multiplied by

## Slide 13: Irrigation Demand Scenarios and assumptions
Two crops are included: Rice and Oil palm trees
Across all sub-basins, the below assumptions are considered for Rice:
15% of the rice cultivated land is assumed to be planted during the ‘dry’ season. 100% of those land are assumed to be irrigated
85% of the rice cultivated land is assumed to be planted during the ‘wet’ season. None of those plantation are assumed to be irrigated
Irrigation efficiency: 36%
Across all sub-basins, the below assumptions are considered for Oil palm trees:
30% of the oil palm tree plantation are assumed to be irrigated
Irrigation efficiency: 36%
Note: irrigation demand shown on these maps does not include the effect of climate change. The projected years refer to the projections in cultivated areas only.

## Slide 14: Irrigation requirement: sensitivity to climate change
Note 1: the star symbols show the ‘no climate change’ scenario.
Note 2: the black lines are isolines of specific changes from the reference ‘no change scenario’.
Simulated irrigation requirement for Rice
Simulated irrigation requirement for oil palm trees
Notes: Name colorbar axis ‘irr requiremewnts’

## Slide 15: Total irrigation demand across the Orinoquia River basin
Irrigated areas as in 2022
Projected irrigated areas as in 2050

## Slide 16: Livestock Demand Scenarios and assumptions
Three animal types are considered: chickens, pigs and cattle
The following assumptions are applied to all sub-basins:
 | Chickens | Pigs | Cattle
Water use per head (m3/year) | 7.3 | 87.4 | 60.2
Table 2: Water use per animal in livestock industries
A loss term equal to 25% is applied

## Slide 17: Consumptive demand (Summary)
 | 2022 | 2030 | 2040 | 2050
Urban | 134.8 | 150.9 (+12%) | 171.0 (+27%) | 191.2 (+42%)
Rural | 30.3 | 32.8 (+8%) | 35.9 (+18%) | 39.0 (+29%)
Irrigation | 2,126.2 | 2,761.1 (+30%) | 3,589.9 (+69%) | 4,442.1 (+109%)
Livestock | 603.8 | 808.3 (+33%) | 1,072.5 (+78%) | 1,340.7 (+122%)
Total | 2,895.1 | 3,753.1 (+30%) | 4,869.3 (+68%) | 6,013.0 (+108%)
Note 1: Values are given in Mm3/year
Note 2 : Percent changes are calculated from the ‘2022’ baseline. Percent values are rounded to the closest integer.

## Slide 18: River flow scenarios

## Slide 19: Streamflow spatial variability
Note: Annual runoff depends on the sub-basin area
Note: Specific runoff highlights sub-basins that generate more runoff per km2
The maps below illustrate the spatial variability of the runoff generation across the Orinoquia River basin. Results are averaged across 5 stochastic realizations. No climate change is assumed.
The map of average specific runoff shows that upstream areas located at higher elevations tends to produce more runoff than lowlands.

## Slide 20: Streamflow: sensitivity to rainfall and temp changes

## Slide 21: Streamflow: sensitivity to rainfall and temp changes

## Slide 22: Streamflow: sensitivity to rainfall and temp changes
The effect of temperature change is negligeable when compared to the effect of change in rainfall

## Slide 23: Environmental flow constraints
Minimum flow requirements are equal to 25% of the average dry season flow (December through March).
Note: The two maps shows the same variable – the unit is different.

## Slide 24: Preliminary results
Visualization of deliveries and demand time series
Variability in space
Climate response function to assess vulnerability

## Slide 25: Time series: Effect of climate change

## Slide 26
Example : Metica sub-basin – FCFS policy – No Climate change - Demand as in 2022
No deficit: black line (deliveries) on top of demand (colors)
Top plot: Dfwu: urban freshwater demand; Dirr: irrigation demand; Dliv: demand for livestock; Dfwr: rural freshwater demand
Bottom plot: To downstream: water volume that flows to the downstream basin; Min flow: minimum flow requirement
Minimum flow requirement is not satisfied during these months

## Slide 27
Example : Metica sub-basin – FCFS policy – +3oC; -20% rainfall- Demand as in 2022
Climate change may lead to significant deficit in deliveries during some years
Deficits in minimum flow requirements are more frequent
Top plot: Dfwu: urban freshwater demand; Dirr: irrigation demand; Dliv: demand for livestock; Dfwr: rural freshwater demand
Bottom plot: To downstream: water volume that flows to the downstream basin; Min flow: minimum flow requirement

## Slide 28: Time series: Effect of demand change

## Slide 29
Example : Metica sub-basin – FCFS policy – No Climate change - Demand as in 2022
Top plot: Dfwu: urban freshwater demand; Dirr: irrigation demand; Dliv: demand for livestock; Dfwr: rural freshwater demand
Bottom plot: To downstream: water volume that flows to the downstream basin; Min flow: minimum flow requirement

## Slide 30
Demand change may lead to an increase in deficit during some years
Example : Metica sub-basin – FCFS policy – No Climate change - Demand as in 2040
Top plot: Dfwu: urban freshwater demand; Dirr: irrigation demand; Dliv: demand for livestock; Dfwr: rural freshwater demand
Bottom plot: To downstream: water volume that flows to the downstream basin; Min flow: minimum flow requirement

## Slide 31: Time series: Effect of different “policies” (order to which the users are served)

## Slide 32
Example : Metica sub-basin – FCFS policy – No Climate change - Demand as in 2022
Top plot: Dfwu: urban freshwater demand; Dirr: irrigation demand; Dliv: demand for livestock; Dfwr: rural freshwater demand
Bottom plot: To downstream: water volume that flows to the downstream basin; Min flow: minimum flow requirement

## Slide 33
Example : Metica sub-basin – PE policy – No Climate change - Demand as in 2022
Top plot: Dfwu: urban freshwater demand; Dirr: irrigation demand; Dliv: demand for livestock; Dfwr: rural freshwater demand
Bottom plot: To downstream: water volume that flows to the downstream basin; Min flow: minimum flow requirement
Enforcing the minimum flow leads to deficit in water deliveries

## Slide 34
Example : Metica sub-basin – PE policy – +3oC; -20% rainfall- Demand as in 2022
Top plot: Dfwu: urban freshwater demand; Dirr: irrigation demand; Dliv: demand for livestock; Dfwr: rural freshwater demand
Bottom plot: To downstream: water volume that flows to the downstream basin; Min flow: minimum flow requirement
With climate change, enforcing the minimum flow is no longer enough to guarantee this objective

## Slide 35: Variability in space – climate change and policies

## Slide 36
Policy FCFS
Policy PE
No climate change Demand as in 2022
+3oC
-20% rainfall
Demand as in 2040
Frequency of annual deficit in minimum flow

## Slide 37
Policy FCFS
Policy PE
No climate change Demand as in 2022
+3oC
-20% rainfall
Demand as in 2040
Frequency of annual deficit in urban deliveries

## Slide 38
Policy FCFS
Policy PE
No climate change Demand as in 2022
+3oC
-20% rainfall
Demand as in 2040
Frequency of annual deficit in rural deliveries

## Slide 39
Policy FCFS
Policy PE
No climate change Demand as in 2022
+3oC
-20% rainfall
Demand as in 2040
Frequency of annual deficit in irrigation deliveries

## Slide 40
Policy FCFS
Policy PE
No climate change Demand as in 2022
+3oC
-20% rainfall
Demand as in 2040
Frequency of annual deficit in livestock deliveries

## Slide 41: Climate response function to assess vulnerability

## Slide 42
Illustration with Metica sub-basin

## Slide 43: Freshwater urban deliveries

## Slide 44
Effect of precipitation change (x-axis) and temperature change (colors) on the frequency of annual in urban freshwater deficit.
Demand as in 2040
Policy FCFS
Policy PE

## Slide 45
Effect of precipitation change (colors) and temperature change (x-axis) on the frequency of annual in urban freshwater deficit.
Demand as in 2040
Policy FCFS
Policy PE

## Slide 46
Effect of precipitation change (x-axis) and demand change (colors) on the frequency of annual deficit in urban freshwater deliveries.
No temperature change
Policy FCFS
Policy PE

## Slide 47
Effect of climate and policy change (Metica)
Urban demand – Demand as in 2040
Warning: color bars are different for the two scenarios

## Slide 48: Irrigation water supply

## Slide 49
Effect of precipitation change (x-axis) and temperature change (colors) on the frequency of annual deficit in irrigation deliveries.
Demand as in 2040
Policy FCFS
Policy PE

## Slide 50
Effect of precipitation change (colors) and temperature change (x-axis) on the frequency of annual deficit in irrigation deliveries.
Demand as in 2040
Policy FCFS
Policy PE

## Slide 51
Effect of precipitation change (x-axis) and temperature change (colors) on the frequency of annual deficit in irrigation deliveries.
No change in temperature
Policy FCFS
Policy PE

## Slide 52
Effect of climate and policy change (Metica)
Agricultural demand – Demand as in 2040
Warning: color bars are different for the two scenarios

## Slide 53: Livestock water deliveries

## Slide 54
Effect of precipitation change (x-axis) and temperature change (colors) on the frequency of annual deficit in livestock water deliveries.
Demand as in 2040
Policy FCFS
Policy PE

## Slide 55
Effect of precipitation change (colors) and temperature change (x-axis) on the frequency of annual deficit in livestock water deliveries.
Demand as in 2040
Policy FCFS
Policy PE

## Slide 56
Effect of precipitation change (x-axis) and temperature change (colors) on the frequency of annual deficit in livestock water deliveries.
No change in temperature
Policy FCFS
Policy PE

## Slide 57
Effect of climate and policy change (Metica)
Livestock demand – Demand as in 2040
Warning: color bars are different for the two scenarios

## Slide 58: Rural freshwater deliveries

## Slide 59
Effect of precipitation change (x-axis) and temperature change (colors) on the frequency of annual deficit in rural freshwater deliveries.
Demand as in 2040
Policy FCFS
Policy PE

## Slide 60
Effect of precipitation change (colors) and temperature change (x-axis) on the frequency of annual deficit in rural freshwater deliveries.
Demand as in 2040
Policy FCFS
Policy PE

## Slide 61
Effect of precipitation change (x-axis) and temperature change (colors) on the frequency of annual deficit in rural freshwater deliveries.
No change in temperature
Policy FCFS
Policy PE

## Slide 62
Effect of climate and policy change (Metica)
Rural demand – Demand as in 2040
Warning: color bars are different for the two scenarios

## Slide 63: Minimum flow requirements

## Slide 64
Effect of precipitation change (x-axis) and temperature change (colors) on the frequency of annual deficit in minimum flow requirement deliveries.
Demand as in 2040
Policy FCFS
Policy PE

## Slide 65
Effect of precipitation change (colors) and temperature change (x-axis) on the frequency of annual deficit in minimum flow requirement deliveries.
Demand as in 2040
Policy FCFS
Policy PE

## Slide 66
Effect of precipitation change (x-axis) and temperature change (colors) on the frequency of annual deficit in minimum flow requirement deliveries.
No change in temperature
Policy FCFS
Policy PE

## Slide 67
Effect of climate and policy change (Metica)
Environmental flow – Demand as in 2040
Warning: color bars are different for the two scenarios

## Slide 68
Visualizing trade-offs among water users
Parallel coordinates plot: a useful tool for visualizing high-dimension dataset
Scenarios / assumptions
Performance metrics

## Slide 69
Visualizing trade-offs among water users
Parallel coordinates plot: a useful tool for visualizing high-dimension dataset
Scenarios / assumptions
Performance metrics
Change in temperature

## Slide 70
Visualizing trade-offs among water users
Parallel coordinates plot: a useful tool for visualizing high-dimension dataset
Scenarios / assumptions
Performance metrics
Change in precipitation

## Slide 71
Visualizing trade-offs among water users
Parallel coordinates plot: a useful tool for visualizing high-dimension dataset
Scenarios / assumptions
Performance metrics
Freshwater demand scenario

## Slide 72
Visualizing trade-offs among water users
Parallel coordinates plot: a useful tool for visualizing high-dimension dataset
Scenarios / assumptions
Performance metrics
Irrigation demand scenario

## Slide 73
Visualizing trade-offs among water users
Parallel coordinates plot: a useful tool for visualizing high-dimension dataset
Scenarios / assumptions
Performance metrics
Livestock demand scenario

## Slide 74
Visualizing trade-offs among water users
Parallel coordinates plot: a useful tool for visualizing high-dimension dataset
Scenarios / assumptions
Performance metrics
Annual frequency in urban water delivery (%)

## Slide 75
Visualizing trade-offs among water users
Parallel coordinates plot: a useful tool for visualizing high-dimension dataset
Scenarios / assumptions
Performance metrics
Annual frequency in rural water delivery (%)

## Slide 76
Visualizing trade-offs among water users
Parallel coordinates plot: a useful tool for visualizing high-dimension dataset
Scenarios / assumptions
Performance metrics
Annual frequency in livestock water delivery (%)

## Slide 77
Visualizing trade-offs among water users
Parallel coordinates plot: a useful tool for visualizing high-dimension dataset
Scenarios / assumptions
Performance metrics
Annual frequency in irrigation water delivery (%)

## Slide 78
Visualizing trade-offs among water users
Parallel coordinates plot: a useful tool for visualizing high-dimension dataset
Scenarios / assumptions
Performance metrics
Annual frequency in minimum flow requirement (%)

## Slide 79
Visualizing trade-offs among water users
Parallel coordinates plot: a useful tool for visualizing high-dimension dataset
Scenarios / assumptions
Performance metrics
Each line shows a unique combination of assumption values along the parallel axes and indicated the associated performance metrics obtained for those assumptions/scenarios.
For example, the lines highlighted with green and orange colors are two combinations of scenarios/assumptions leading to two very different performance for the system

## Slide 80
Visualizing trade-offs among water users
Parallel coordinates plot: a useful tool for visualizing high-dimension dataset
Scenarios / assumptions
Performance metrics
By default:
blue color shows the result obtained using the Policy Enforced (PE) assumption
red color shows the results obtained with the First Come First Served (FCFS) assumption)

## Slide 81
Visualizing trade-offs among water users
Parallel coordinates plot: a useful tool for visualizing high-dimension dataset
We can select the range of some values (shown I pink color on the assumption axes)
The scenarios discarded given the selected values on the axes are shown with grey colors.

## Slide 82
Visualizing trade-offs among water users
Parallel coordinates plot: a useful tool for visualizing high-dimension dataset
A nice feature of parallel coordinates plot is that they are interactive.
The figure shows up on the user’s web browser, who can then select the basin for which results are shown and modify the range of the axis values to be highlighted.
See a demo during the presentation